## Slide 1
Multiple Antenna Communications
Lecture 14:
Practical Aspects and Outlook
Emil Björnson

## Slide 2: Outline
Role of multiple antenna communications
  Enhanced data rates
  Reliability and coverage
Practical aspects
  Analog, digital, hybrid beamforming
  Polarization, subarrays, 3D beamforming
Outlook towards the future

## Slide 3: Data traffic grows exponentially
EB/month
4G
3G
2G
5G
More traffic per device
Require higher data rate
Users active more often
Data: Ericsson Mobility Report 2021
Impact of multiple antenna communications?
45% annual growth

## Slide 4: Point-to-point MIMO: Better user performance
Beamforming and multiplexing gain

## Slide 5: Multi-user MIMO: Spatial multiplexing of users
Few antennas (elements): Broad beams
Massive number of antennas: Narrow beams
Serve many users at same time/frequency resource
Narrow beams limit interference

## Slide 6: Beyond enhanced data rate
Ultra-reliable low-latency communication (URLLC)
  Channel hardening alleviates channel fading
  Fewer retransmissions, predictable performance
Massive machine-type communication (mMTC)
  Extend coverage, more cost-efficient deployment
  Reduce transmit power for battery-power devices

## Slide 7: Passive and active antennas
Can be placed in an edge cloud
Passive
antenna
Passive
antenna
Array of active antennas:
Antenna-integrated radios
Massive
MIMO
Evolution:
Radio = Also called transceiver chain
BBU = Baseband unit

## Slide 8: Beamsteering and (generalized) beamforming
Beamsteering
Beam in one angular direction
Not associated with any user
Beamforming
Beam in one angular direction
Designed for line-of-sight user
Generalized beamforming
Superposition of beams
Designed for a non-line-of-sight user

## Slide 9: Digital beamforming
Full flexibility to create a superposition of beams
Adapt to multipath
Vary power over antennas
Vary over frequency domain
Precoding
Multi-user/layer beamforming

## Slide 10: Analog and hybrid beamforming
Analog beamforming
One signal, different phase shifts
Same over frequency domain
Hybrid beamforming
Create a few beams, perform digital beamforming over them

## Slide 11: Beamforming and multiplexing gains
Two antennas:
2x signal signal
Four antennas:
4x signal gain
Four antennas, two signals:
Divide power between two beams
4x signal gain
Two antennas, two signals:
Divide power between two beams
2x signal gain

## Slide 12: Three-dimensional beamforming
Array geometry determines possible beam directions
Horizontal linear array Azimuth beamforming
Vertical linear array Elevation beamforming
Planar array 3D beamforming

## Slide 13: Polarization of waves and antennas
Channel is changing the polarization
Anyway creates an extra dimension
Often used in point-to-point MIMO
Horizontally
polarized
Vertically
polarized
slant
polarized
slant
polarized

## Slide 14: Typical channel properties
People live on the ground
  Builds have limited height
Coverage sector:
120 degrees
Smaller angular interval
Horizontal beamforming is most important

## Slide 15: Planar arrays and subarrays
128 antenna elements
How many radios?
64 radios
(64T64R)
32 radios
(32T32R)
“Antenna” = Group of elements sharing one radio (transceiver chains)

## Slide 16: Evolution of active antenna technology
Passive sector antenna
8 elements (7 dBi each)
1 transceiver chain
Fixed beam 16 dBi
Classical antenna array
64 elements (32 per polarization)
8 transceivers (2 per column)
Up to 8 horizontal beams
Massive antenna array
128 elements (64 per polarization)
64 transceiver
Up to 64 3D beams
1 antenna
8 antennas
64 antennas

## Slide 17: Massive MIMO in 5G
64 antennas
Photo: Erik G. Larsson, May 2018

## Slide 18: Massive MIMO in 5G: Evolution
Ericsson AIR 3268
3.5 GHz band
32 antennas (128 elements)
12 kg
200 W over 200 MHz
Integrated circuitry
Ericsson Street Macro 6705
Millimeter-wave band
Complete base station

## Slide 19: What might happen in the future?
New deployment concepts
1) Distributed Massive MIMO
(Cell-free)
3) Physically large arrays
2) Reconfigurable intelligent surfaces
64-antenna
Massive MIMO

## Slide 20: What have we not covered in the course?
Point-to-point MIMO
  Cases with imperfect channel knowledge
Massive MIMO
  Advanced processing (multi-cell, MMSE)
  More realistic channels (e.g., correlated Rayleigh fading)
Fading channels
  Gradual variations, channel tracking and prediction

## Slide 21
Multiple Antenna Communications
Lecture 14:
Practical Aspects and Terminologies
Emil Björnson